## Slide 1: Semester Projects - proposals -
A.A. 2024/2025
Measurement for Automation and Industrial Production (MAIP)

## Slide 2: Proposal #1
Hardware:
Two FS1012-1100-NG and FS2012 transducers;
Electronic signal conditioning circuit to be developed;
One Mod.NEO – pp2 air pump;
Laboratory benchtop power supply;
GPIB to USB adapter;
PC with embedded NI DAQ board.
Software:
LabVIEW
Development of an automated measurement system for characterizing of an
air flow transducer

## Slide 3
Proposal #1
Objectives to be achieved by the students
Calibration phase:
  Description and discussion of FS1012 and FS2012 transducers;
  Description and discussion of calibration method;
  Description and discussion of the Mod.NEO – PP2 air pump;
  Description and discussion of characterization method for the FS1012 transducer;
  Description of the differences between the datasheet characterization reported curve and the obtained curve during the characterization phase in the lab;
Development of a VI which is able to do:
  the signal acquisition from the FS1012 transducer signal conditioning circuit;
  the signal acquisition from the FS2012 transducer signal conditioning circuit;
  Calibration of the FS1012 transducers versus the calibrated FS2012 transducer;
  Control of the PP2 air pump by means a programmable benchtop laboratory power supply;
  Display of the air flow from the FS1012 transducer and the FS2012 transducer in real-time.

## Slide 4
Laboratory benchtop
power supply
Signal conditioning circuit
Proposal #1
Block diagram
Neo PP2
air pump
PC:
LabVIEW
FS2012
FS1012
Air flow input port
Air flow output port
GPIB
DAQ NI 6008 card
USB

## Slide 5
The FS1012-1100-NG transducer:
Proposal #1
Components
Mod.NEO – pp2 air pump:
http://www.ead-pumps.com/html/PDF/NEOP-P3.pdf
The FS2012 calibrated transducer:
https://www.renesas.com/en/products/sensor-products/flow-sensors/fs2012-gas-or-liquid-flow-sensor-module-calibration
https://www.renesas.com/en/products/sensor-products/flow-sensors/fs1012-gas-or-liquid-flow-sensor-module

## Slide 6: Proposal #2
Hardware:
Two Sharp GP2Y0A41SK0F transducers;
Electronic signal conditioning circuit to be developed;
Mechanical test-bench to be developed for 30 cm distance range;
Twentieth caliber;
PC with embedded NI DAQ board.
Software:
LabVIEW
Development of an automated measurement system for differential distance measurement based on two Sharp GP2Y0A41SK0F optical transducers

## Slide 7
Proposal #2
Objectives to be achieved by the students
Calibration phase:
  Description and discussion of GP2Y0A41SK0F transducer;
  Description and discussion of calibration method using a twentieth caliber as reference instrument for distance measurement in differential mode;
  Description and discussion of characterization method for the GP2Y0A41SK0F transducer;
  Description of the differences between the datasheet characterization reported curve and the obtained curve during the characterization phase in the lab;
Development of a VI which is able to do:
  Signal acquisition from the GP2Y0A41SK0F transducers signal conditioning circuit;
  Calibration of the GP2Y0A41SK0F transducers versus reference distance measurement instrument (the twentieth caliber);
  Display of the distance in real-time.

## Slide 8
Power supply and control circuit
Signal conditioning circuit
Proposal #2
Block diagram
PC:
LabVIEW
GP2Y0A41SK0F
GP2Y0A41SK0F
DAQ NI 6008 card
USB

## Slide 9
The GP2Y0A41SK0F transducer:
Proposal #2
Components
GP2Y0A41SK0F
GP2Y0A41SK0F
30 cm active sensing area
Moving direction
https://www.mouser.it/datasheet/2/365/gp2y0a41sk_e-594157.pdf

## Slide 10: Proposal #3
Hardware:
Resistive level sensor PN-12110215TC-X;
Electronic signal conditioning circuit to be developed;
Mechanical test-bench to be developed for 20 cm level range;
Graduated cylinder;
PC with embedded NI DAQ board.
Software:
LabVIEW
Development of an automated measurement system for characterizing of a
resistive level sensor

## Slide 11
Proposal #3
Objectives to be achieved by the students
Calibration phase:
  Description and discussion of resistive level sensor;
  Description and discussion of calibration method for liquid level measurement;
  Description and discussion of characterization method for the resistive level sensor;
  Description of the differences between the datasheet characterization reported curve and the obtained curve during the characterization phase in the lab using the graduated cylinder;
Development of a VI which is able to do:
  Signal acquisition from the resistive level sensor signal conditioning circuit;
  Calibration of the resistive level sensor versus reference level measurement instrument (the graduated cylinder);
  Level display in real-time.

## Slide 12
Power supply
Signal conditioning circuit
Proposal #3
Block diagram
PC:
LabVIEW
resistive level sensor
DAQ NI 6008 card
USB

## Slide 13
The resistive level sensor PN-12110215TC-X :
Proposal #3
Components
Cylinder with water
Resistive level sensor
https://img1.wsimg.com/blobby/go/6e1bce17-f4fa-40c3-9d89-9bb7445697bb/downloads/Standard%20eTape%20Data%20Sheet.pdf